SUPER MORSE (TM)
     
     
                                   ADVANCED TOPICS
     
                                       Ver. 4.16
     
     
                                   Copyright 1994-95
                                     M. Lee Murrah
     
                                        3-25-95
     
     
     
     1. How Morse Code Is Defined..................................   1
          a. DITS and DAHS.........................................   1
          b. Morse Characters......................................   1
          c. Code Weighting........................................   4
          d. Code "Speed"..........................................   4
          e. The "Farnsworth" Method...............................   5
     2. Learning the Morse Code....................................   6
          a. The Super Morse Teaching Method.......................   6
          b. Studying Hints........................................   6
     3. Scripted Disk Files........................................   7
          a. The Message Command...................................   8
          b. The Pause Command.....................................   8
          c. Set Speeds Command....................................   8
          d. Restore Speeds Command................................   8
          e. Speed Lock Commands...................................   9
     4. Customization of External Files............................   9
          a. General...............................................   9
          b. Data Files............................................   9
          c. License Classes File..................................  10
          d. Text Files............................................  10
     5. QSO Templates..............................................  11
     6. Equipment and System Requirements and Limitations..........  12
          a. System Configuration..................................  12
          b. Mouse.................................................  12
          c. Code Speed Calibration................................  12
          d. Video Display Card....................................  13
          e. Disk Cache Programs...................................  13
          f. Floppy Disk Write Protect Tabs........................  13
          g. Windows Capability....................................  13
          h. Speaker Volume........................................  13
     7. Sound Boards...............................................  14
     8. Interfacing External Equipment.............................  14
     9. Circuit Diagrams for External Connections..................  16
          a. Using an External Hand Key............................  16
          b.  Connecting to a Receiver.............................  16
          c. Driving a Transmitter or Other Device.................  16
          d. Using a Volume-Controlled Headphone...................  18
          e. Using an External Oscillator..........................  19
          f. Using an External Sound Output........................  20




                                                                      Page 1

          This file contains information on selected advanced
     features of Super Morse. See QUICK.DOC for basic information and
     overview of Super Morse.
     
     
     1. How Morse Code Is Defined
     ----------------------------
     
          a. DITS and DAHS
          ----------------
     
          Morse code is a sound language that uses two different
     lengths of a single tone in various combinations to represent
     all the characters of the Morse alphabet. These two tones are
     distinguished by their length, one a "short" tone and t he other
     a "long" tone. The short tone is phonetically referred to as
     "DIT", and the long tone as "DAH".  "DIT" is usually written as
     "DI" when it is not the last element of a character. You will
     often see the short tone represented as a "." (dot) and the long
     tone as a "-" (dash), but it is commonly agreed that use of these
     symbols encourages a visual approach to the code, which slows
     code learning.  You should never think of the Morse code as dots
     and dashes or write it in that way!
     
          The original Morse code as used in landline telegraphy was
     represented by a combinations of timed clicks.  However, when
     radio came into use, the code was revised to use tones which are
     more suited for radio use. The original Morse code is used in la
     nd telegraphy is called the American Morse code, but the code now
     commonly used in radio is called the International Morse code.
     
          b. Morse Characters
          -------------------
     
          The amateur radio Morse code set is a subset of the
     International Morse code.  It uses a reduced character set of
     the 26 letters, the 10 numerals, 4 punctuation marks and 5
     special procedure signs.  The Morse character set supported by
     Super Morse is shown in the several figures that follow.
     


                                                                      Page 2

          The printable Morse characters are shown in the following
     table:
     
                  A  DIT DAH           N  DAH DIT
                  B  DAH DIT DIT DIT   O  DAH DAH DAH
                  C  DAH DIT DAH DIT   P  DIT DAH DAH DIT
                  D  DAH DIT DIT       Q  DAH DAH DIT DAH
                  E  DIT               R  DIT DAH DIT
                  F  DIT DIT DAH DIT   S  DIT DIT DIT
                  G  DAH DAH DIT       T  DAH
                  H  DIT DIT DIT DIT   U  DIT DIT DAH
                  I  DIT DIT           V  DIT DIT DIT DAH
                  J  DIT DAH DAH DAH   W  DIT DAH DAH
                  K  DAH DIT DAH       X  DAH DIT DIT DAH
                  L  DIT DAH DIT DIT   Y  DAH DIT DAH DAH
                  M  DAH DAH           Z  DAH DAH DIT DIT
     
     
               1  DIT DAH DAH DAH DAH     6  DAH DIT DIT DIT DIT
               2  DIT DIT DAH DAH DAH     7  DAH DAH DIT DIT DIT
               3  DIT DIT DIT DAH DAH     8  DAH DAH DAH DIT DIT
               4  DIT DIT DIT DIT DAH     9  DAH DAH DAH DAH DIT
               5  DIT DIT DIT DIT DIT     0  DAH DAH DAH DAH DAH
     
          The International Morse code that is used in amateur radio
     supports a number of punctuation marks, but the amateur subset
     uses only the five shown below:
     
                       .  DIT DAH DIT DAH DIT DAH
                       ,  DAH DAH DIT DIT DAH DAH
                       ?  DIT DIT DAH DAH DIT DIT
                       /  DAH DIT DIT DAH DIT
                       -  DAH DIT DIT DIT DIT DAH
     
          Morse code communications uses several special characters
     that convey procedural information in shorthand.  These are often
     longer characters that can be viewed as combinations of
     alphabetic characters without an intervening character space. The
     most common of these procedure signs, or "prosigns", used in
     amateur radio are shown below:
     
              Prosign          Meaning
              -------          -------
                <AA>           New line
                <AR>           End of message
                <AS>           Wait, stand-by
                <BT>           Double Dash ("=")
                <KN>           Over-specified station only
                <KA>           Attention
                <SK>           End of contact
                <SN>           Understood
     
     <KA> and <SN> along with <BT> are frequently used in traffic
     handling.


                                                                      Page 3

     


                                                                      Page 4

          Several international characters are used in Morse code,
     especially in Europe.  These characters shown in Fig. 1-3. are
     also supported by Super Morse in some modes:
     
                 ASCII     Identification
                 -----     --------------
                   129       {Double dotted "u"}
                   130       {Forward accented "e"}
                   143       {Dotted "a"}
                   146       {Double dotted "a"}
                   157       {Double dotted "o"}
                   164       {tilde "n"}
     
          c. Code Weighting
          -----------------
     
          The various elements of Morse code are defined in relation
     to each other. The DIT is assigned the shortest duration and is
     defined as being one time unit in duration, and a DAH is 3 times
     as long as a DIT, or 3 time units in duration.  The silence
     between DITs and DAHs in a character, which we will call an
     "element space" is the same length as a DIT, i.e., one time unit
     in duration.  The silence between characters, which we will call
     a "character space", is 3 time units in duration. Finally, the
     space between words, which we will call a "word space" is 7 time
     units in duration.
     
          Perfectly sent code uses these standard relationships, but
     code is not usually perfectly sent except when a computer is
     used. Each person who sends code manually, develops a weighting
     slightly different from the standard, and this unusual weighting
     is said to constitute the operator's very recognizable "fist".
     
          Operators who use automatic keyers can usually set the
     weighting as a personal preference.  Weighting very far from the
     standard sounds choppy and hard to copy.
     
          d. Code "Speed"
          --------------
     
          The speed of Morse code is measured in words per minute
     (WPM). Code speed is an elusive measure since words are of
     various lengths; and when random characters are being sent, there
     are no words at all!
     
          Code speed has therefore been arbitrarily defined by
     standard words.  The standard word for plain text is "PARIS",
     which, if you add up the time units in all the code sound
     elements used to send "PARIS" (DITs, DAHs, and spaces between the
     DIT's and D AHS, characters and words), you will find that it is
     50 units of time long.  One word per minute is defined as sending
     "PARIS" using code elements timed to fill one minute, including


                                                                      Page 5

     the word space following the last word.  Ten words per minute
     would be sent at a speed necessary to send "PARIS" 10 times in
     one minute.  The code elements are calibrated at any particular
     speed against "PARIS", and when text is sent at, say, 10 words
     per minute, more or fewer actual words may be sent depending upon
     their length.
     
          The word "PARIS" will not work for random characters since
     the average Morse code character used to send English text is
     shorter than the average character used to send random
     characters.  This is because English does not use all the letters
     in equal numbers and because Morse code assigns the shortest
     codes to the most frequently used letters in English.  The most
     frequently used letter in English is "E", and it is assigned the
     shortest code, the DIT.  A less frequently used letter such as
     "Q" is assigned a longer code, DAH DAH DI DAH.
     
          For random characters, therefore, the standard word "CODEX"
     was chosen. If you analyze "CODEX", you will find that it
     contains 60 code elements. The effect of this difference is that
     the DITS and DAHS in randomly sent characters should sound about
     20% shorter than those in plain text at the same nominal speed.
     Randomly sent characters therefore should sound 20% faster that
     plain words.  This is the reason that manufacturers of code
     tapes can boast that the actual test will seem slow after using
     their random character tapes!
     
          e. The "Farnsworth" Method
          --------------------------
     
          Morse code is usually sent with the standard relationship
     between character spaces and the elements which make up the
     character.  In other words, the DITS, DAHS and element spaces are
     sent according to the same speed standa rd.  However, Farnsworth
     discovered that code learning can be accelerated if the DITs,
     DAHs and element spaces are compressed as if the code were being
     sent at a high speed while the character spaces are expanded to
     maintain an overall lower send speed. This is called the
     "Farnsworth method", and it is endorsed by the ARRL as the best
     way to learn the code.
     
          The Farnsworth method is supported and is used as the
     default method by Super Morse.  Two Farnsworth speeds are
     provided.  The "Lo" Farnsworth speed, preset at 18 WPM, is used
     at send speeds below 20 WPM; and the "Hi" Farnsworth speed,
     preset at 26 WPM, is used above 20 WPM. Beware, however, that not
     all code tests are given in the Farnsworth format, or, if they
     do, using these speeds! Check with your testing coordinator to
     determine which method will be used, and then use that system
     when studying with Super Morse.
     
     


                                                                      Page 6

     2. Learning the Morse Code
     --------------------------
     
          a. The Super Morse Teaching Method
          ----------------------------------
     
          Unlike standard Morse code teaching methods, Super Morse
     does not begin by introducing characters. Instead Super Morse
     starts with sounds only -- characters are not taught or displayed
     in the early lessons.  The idea is to emphasize that Morse code
     is a sound language and to teach the fundamentals of code sounds.
     Two sound-only exercises are provided. First, the basic DIT and
     DAH sounds are taught. Second, Super Morse puts the basic sounds
     together into the four fundamental two-sound combinations.
     
          Only after the basic sounds and sound combinations are
     taught does Super Morse start identifying characters.  Before the
     standard code groups are introduced, code "steps", which are
     groups of two similarly sounding characters, are sent to
     gradually i ntroduce the characters in pairs. The idea is to
     teach the student to distinguish similar sounding characters from
     the beginning, such that those which do not sound so much alike
     will fall into place by themselves.  Also the characters are
     slowly learned in an indirect fashion in that the student is
     encouraged to concentrate on the differences rather than the
     content of the characters themselves. Only when the steps are
     completed are the standard code groups introduced.
     
          The Learn selections "DIT/DAH" through "Levels" are ordered
     to slowly build up your knowledge of the characters in a very
     logical way.  It is recommended that the Learn subcommands be used
     in the same order as the selections are presented.
     
          b. Studying Hints
          -----------------
     
          There is no one best way to learn the Morse code.  As with
     foreign languages (to which Morse code is similar in some ways),
     some people can learn the code faster than others.  The best
     attribute that one can possess in learning the code is
     persistence.
     
          Super Morse implements one method of learning the Morse
     code.  If you follow the lessons provided in the Learn phase, you
     should have no trouble in learning the Morse code in a few weeks
     or months.
     
          In addition to the method provided by Super Morse several
     general tips on learning the Morse code can be provided as
     follows:
     
          i.  Learn the characters by sound, not by sight.  Each of
     the characters has its own characteristic length and rhythm.  Do
     not memorize the characters using the visual dot and dash


                                                                      Page 7

     symbols.  That will only slow you down and create bad habits that
     will be very hard to break!
     
          ii.  Set the character speed to 13 words per minute or
     higher (the ARRL uses 18 WPM) and the send speed at whatever
     lower speed you desire. (Super Morse automatically sets the
     character speed to 18 WPM). Since your ultimate goal is 13 words
     per minute , it is much better to learn the sounds of the
     characters at the higher speed even though they are spaced at a
     lower speed. As mentioned above this is called the Farnsworth
     method, and it helps to eliminate the "hump" that most people
     experience around 10 words per minute.
     
          iii.  Study every day, but if you feel you are stuck and
     not making progress, take a few days off.  It's amazing how this
     will sometimes clear your head.
     
          iv.  Try to copy code in you head as much as possible.
     
          v.  Obtain access to a ham receiver and try to copy real
     transmissions off the air.  Some general coverage short wave
     receivers permit reception of Morse code, but in general they
     are harder to tune in on a Morse code signal.
     
          vi.  As soon as possible learn the sounds of whole words.
     You will find that whole words have characteristic lengths and
     rhythms that distinguish them from all other words.
     
          vii.  Turn on the Super Morse Build/Groups function and let
     the computer send in the background while you are doing something
     else, such as reading a book or working on a construction
     project.  Try to identify characters while doing the other
     activity. This will help your brain shift to "automatic" and will
     help the code sounds become a natural "part of the wallpaper."
     
          viii.  Although the code test no longer requires that you
     demonstrate an ability to send Morse code, you should get a code
     practice oscillator and practice your sending.  Note that Super
     Morse can be used as a code practice oscillator using one of
     several keys on the keyboard or an external telegraph key.
     
          ix.  As soon as you pass the novice test, get a rig on the
     air and operate on the novice bands.  Nothing will increase your
     speed and concentration as well as the pressure of an on-the-air
     contact.  Don't worry about being perfect--the other guy is
     probably in the same boat as you.
     
     3. Scripted Disk Files
     ----------------------
     
          The disk files that may be played with the Build|File
     command amy be scripted by inclusion of commands that control the
     operation of Super Morse. Scripted files permit Super Morse to be


                                                                      Page 8

     automated for special learning methods, to prepare code tapes, or
     to give tests.
     
          Disk files are "scripted" by placing a period (".") in the
     first column of any line followed by a command character in
     capitals and a space and text, if applicable.  With scripting
     Super Morse follows exactly the same line spacings as are used in
     the script file. Thus, if you want lines skipped before and after
     the message, place blank lines in your script file.
     
          Scripting permits the following commands to be inserted in
     a file.
     
          a. The Message Command
          ----------------------
     
          The "M" command line as follows causes the <text> to be
     printed in highlight on the screen:
     
                    .M This a message to the user
     
     This will print "* This is a message to the user" on the screen.
     
          b. The Pause Command
          --------------------
     
          The same effect as the message command, except with a pause
     for you to press a key to continue, is provided by the "P"
     command as follows:
     
                    .P Ask the user to do something
     
     This will print "* Ask the user to do something" and instruct
     you to press any key to continue.
     
          c. Set Speeds Command
          ---------------------
     
          Speeds can be programmed into the script at the indicated
     send speed ("<ss>"), character speed ("<cs>") and word speed
     ("<ws>") with the "S" command as follows:
     
                    .S <ss> <cs> <ws>
     
          d. Restore Speeds Command
          -------------------------
     
          The set speeds command automatically saves the current code
     speed before it is changed.  The former speeds can be restored
     with the following command:
     
                    .R
     


                                                                      Page 9

          e. Speed Lock Commands
          ----------------------
     
          The set speed keys can be disabled with the .L command and
     re-enabled with the .U command.  These commands are not followed
     by text.
     
     
     4. Customization of External Files
     ----------------------------------
     
          a. General
          ----------
     
          In addition to internal modifications, Super Morse permits
     customization by changing the contents of Super Morse's text
     files. Modifiable files all have the "SM" extension, such as
     NAMES.SM.
     
          If a word processor is used, the output must be ASCII text
     only!  Most modern word processors output not only the text that
     you enter in the document but also formatting information which
     is not displayed on the screen. This invisible formatting
     information will cause to Super Morse produce garbage. If you
     use a word processor, be sure to check your user manual to
     determine how to save text in plain ASCII format without the
     formatting information.
     
          b. Data Files
          -------------
     
          Super Morse uses several files containing names, cities,
     and other information used in QSO generation (simulated radio
     contact), and other files for words used in word-based functions.
     If you are not satisfied with the contents of these files, you
     may change them to suit your tastes. Non-U.S. users will probably
     want to change the contents of the states file to include the
     provinces in their own country or other countries.
     
          All data files require that only one item be placed on a
     line starting in column 1 (not at the left margin of a word
     processor file if the margin is shown!) and that no blank lines
     be inserted in the middle of the file.
     
          The names, antenna types, city names, and rig types can be
     changed to reflect your desires by editing the files ANTENNAS.SM,
     NAMES.SM, CITIES.SM, RIGS.SM, and JOBS.SM as described earlier in


                                                                      Page 10

     this document. The maximum number and length of the entries are
     as follows:
     
                    File           Max. Entries   Max. Length
     
                    ANTENNAS.SM          50              15
                    CITIES.SM           200              15
                    JOBS.SM             100              20
                    NAMES.SM            200              10
                    RIGS.SM             100              15
                    STATES.SM           100              15
     
          c. License Classes File
          -----------------------
     
          The only data file having a special format is the
     CLASSES.SM file.  This file contains three lines in a special
     order. The file distributed with Super Morse defines the United
     States license classes and speeds as follows:
     
                                   05 Novice
                                   13 General
                                   20 Advanced
     
          The format is critical!  It must contain three lines and
     start in column 1 (not the left margin of a word processor
     file!). Each line begins with a speed in words per minute in
     columns 1 and 2, followed by a space, followed in column 4 by the
     name of the license class beginning at that speed, not exceeding
     8 characters in length.  If a speed is less than 10 WPM, a "0"
     must be placed at the beginning.  If only two license classes are
     used in your country, repeat the second class definition on the
     third line as in the following generic example:
     
                                   07 Junior
                                   11 Senior
                                   11 Senior
     
          If you have only one class of license, place the same
     information on all three lines.  If your country uses more than
     three classes of licenses, please let me know, and I will expand
     this file.
     
          d. Text Files
          -------------
     
          In some features Super Morse permits you to use a plain
     ASCII text file as input.  An example in the Disk File command in
     the Build phase.  These files should be created with a text
     editor or word processor in the ASCII output mode as described
     above.  The lines in these files can be any length and can start
     in any column.
     
     


                                                                      Page 11

     5. QSO Templates
     ----------------
     
     
          The external template may be selected in the Generate exam
     function. The external template is contained in a disk file
     named QSOn.SM where "n" is a number from 1 to 99.  The file
     QSO1.SM is provided as an example, but you may created other
     ASCII files yourself.
     
          An exam QSO template file comprises any desired text built
     around up to 20 pieces of randomly selected data.  When data is
     desired in the QSO file, insert the identifying number of the
     data type surrounded by curved brackets ("{" and "}").  The
     identifying numbers are as follows:
     
     
          1 - calling station      11 - countries worked
     
     
          2 - responding station   12 - band 1
     
     
          3 - rst report           13 - band 2
     
     
          4 - name                 14 - job
     
     
          5 - city                 15 - rig type
     
     
          6 - state                16 - antenna type
     
     
          7 - age                  17 - antenna height
     
     
          8 - years a ham          18 - power (watts)
     
     
          9 - license class        19 - weather
     
     
          10 - states worked       20 - temperature (Deg. F)
     
     
          The following is an example of a line in a QSO template:
     
     
                    My name is {4}, and I live in {5},{6}.
     
     


                                                                      Page 12

          Super Morse randomly generates a name and substitutes it
     for {4} and a city and state and substitutes them for {5} and
     {6}.  An example of the result is as follows:
     
     
                 My name is Joe, and I live in Northfield, KS.
     
          At least 10 pieces of data should be used in any exam file
     to support the 10 questions that are asked in the exam.
     
     6. Equipment and System Requirements and Limitations
     ----------------------------------------------------
     
          a. System Configuration
          -----------------------
     
          Your CONFIG.SYS file should authorize at least 20 files.
     This can be done with the following statement:
     
                              FILES = 20
     
          b. Mouse
          --------
     
          Super Morse supports a Microsoft mouse.  In some
     configurations, Super Morse uses two serial ports. If you use a
     serial mouse, there may be a conflict.  To fully use all Super
     Morse features, three serial ports are required.
     
          c. Code Speed Calibration
          -------------------------
     
          In order for Super Morse to send properly-timed code,
     calibration to each computer is required.  Calibration is
     affected primarily by the computer clock speed and memory
     resident programs.
     
          Super Morse uses two different calibration methods, (a)
     clock and (b) loop, in order to handle various types of PC
     designs and operating systems. The method that you desire to use
     is selected from the Options menu.
     
          Both methods require some calibration using the Options|Code
     features. The timer method needs to be "tweaked" the first time
     you use it to match itself to your computer, but thereafter it
     self-calibrates to the computer clock speed each time the program
     loads.  However, if you use the loop method, you must calibrate
     Super Morse each time you add or remove a memory resident
     program.
     
          The loop method must be used if your computer does not
     implement the system clock chip in the same way as the original
     PC design, if you are running under Windows as a DOS application,
     or if running on a PC emulator on a MacIntosh or other computer.


                                                                      Page 13

     Super Morse is initially set for the clock method; but if the
     code is erratic or choppy on your computer, you should change to
     the loop method.
     
          d. Video Display Card
          ---------------------
     
          Super Morse supports CGA (color) and MDA (monochrome) video
     displays only.  The proper display adapter can be selected from
     the Options menu. Super Morse will operate on EGA and VGA
     monitors but in the CGA mode.
     
          e. Disk Cache Programs
          ----------------------
     
          Super Morse saves changes in the program parameters when
     you exit the program.  If you are using a disk cache program,
     the parameters may be saved to the cache area in memory and thus
     may not permanently saved to disk.  If you a re having this
     problem, you should try disabling any disk cacheing program which
     you have installed on your system.
     
          f. Floppy Disk Write Protect Tabs
          ---------------------------------
     
          If Super Morse is run from a floppy diskette, a write
     protect tab should not be used! Super Morse must be able to store
     configuration and user information to the diskette.
     
          g. Windows Capability
          ---------------------
     
          Super Morse is written as a DOS program, but it will run
     under Microsoft Windows under certain conditions.  The author
     has confirmed that it will operate under the 386 Extended mode
     (i.e., a 386 or 486 computer is required) using the loop timing
     method.  You must set up a PIF file, and set the background to
     foreground ratio to 10000 to 1 and set Execution to "Exclusive".
     These are available as Advanced options in the PIF editor menu.
     To save you time a PIF file to run Super Morse under the
     conditions stated is provided on the distribution diskette.
     
          h. Speaker Volume
          -----------------
     
          The volume produced by the PC speaker is very low on some
     PC's, but unfortunately there is no way to increase it without
     an external amplifier. Some relief can be obtained by changing
     the speaker tone since speakers (and your ears!) are frequency
     dependent.  ADVICE: Get a Sound Blaster type sound card.  See
     next section for setup.
     


                                                                      Page 14

     7. Sound Boards
     ---------------
     
          Super Morse now supports the Sound Blaster card and
     compatibles. Super Morse initializes for use of the PC speaker,
     and the Sound Blaster must be selected in the Options|Misc menu.
     A sound card is HIGHLY RECOMMENDED!
     
          If you plan to use the Sound Blaster card for sound output,
     you must use a text editor, such as EDIT or EDLIN, (or a word
     processor in ASCII output mode) to insert a line in the
     AUTOEXEC.BAT file specifying an "environment string". The line
     should b e in the following format:
     
               SET BLASTER=A<addr> I<int no> D<DMA channel no> T<SB type>
     
          For a Sound Blaster 1.0 using I/O address 220, Interrupt 7
     and DMA channel 1, the string would look as follows:
     
                         SET BLASTER=A220 I7 D1 T1
     
          The I/O address, Interrupt number, and DMA channel can be
     determined using the TEST-SBC.EXE program provided with your
     Sound Blaster.  If you did not change any of the jumpers on the
     board when you installed it, you can use the factory default
     settin gs shown in the Sound Blaster manual.
     
          The SB type for Sound Blaster and compatible boards for use
     with the "T" parameter is one of the following:
     
                    1 - Sound Blaster 1.5 or earlier
                        Sound Blaster Micro Channel Version
                    2 - Sound Blaster Pro
                    3 - Sound Blaster 2.0
                        Audio Spectrum 16
                    6 - Sound Blaster 16
     
     8. Interfacing External Equipment
     ---------------------------------
     
          The primary I/O for Super Morse code is via the computer
     keyboard and the PC onboard speaker.  Secondary output is
     provided by toggling either the DTR or RTS pin at the selected
     RS-232 communications port.  Input is provided via either the DSR
     o pin at the same port.  You can select whether to expect either
     a high (+) or a low (-) voltage in the key-down condition and
     the opposite in the key-up condition. Output via DTR/RTS is
     available whenever code is being sent, but input via DSR/CTS is
     available only in the Manual key function of the Enhance phase
     and in the Operate phase.
     
          I/O via either COM1, COM2, COM3, or COM4 can be selected
     from the Options|Ports menu selected from the main menu bar. With
     a proper interface DTR/RTS can be used to drive an external


                                                                      Page 15

     oscillator for making high quality code tapes or to key a
     transmitt er. Likewise, DSR/CTS can be interfaced with a hand
     key, electronic keyer, or a receiver.
     
          Code output to the speaker and COM port can be selected
     from the Options menu. Code input can be selected from either one
     of several keys on the computer keyboard or the COM port using
     the Input Keying selection in the Options|Ports menu.
     
          A detailed explanation of how to use the DTR/RTS and
     DSR/CTS signals for the aforementioned purposes is beyond the
     scope of this manual and is left to your ingenuity.  However,
     limited information is provided later in this document. The
     author would like to receive diagrams of tested circuits designed
     by users to take advantage of COM port I/O.
     
          If an external key does not work, check the following:
     
          a. The RS-232 connector pins are small and easily confused.
     Most connectors have the pin numbers beside the pins, but they
     are almost impossible to read without a strong light and
     magnifying glass. Remember that the connector pins on the
     computer ar e a mirror image of those on the cable connector.
     
          b. Some computers connect the RS-232 pins differently.
     Consult your owner's manual, or call your computer manufacturer's
     technical assistance line for information on the configuration.
     Some experimentation (i.e., random poking around in the
     connector) may be required to find the right pins. On the
     author's Gateway 2000, for example, it is necessary to use pin
     20 as signal ground instead of pin 7. This is different from two
     previous computers which used pin 7.
     
          c. The pin numbers given in this manual are for the 25 pin
     DB-25 connector.  If you have a 9 pin DB-9 connector, match the
     pin names instead of numbers.  You will have to consult your
     owner's manual for a definition of the pins for that connector.
     
          d. Super Morse uses two COM ports, and you should make sure
     that different ports are set for the Modem function and the
     keying function.
     
          e. Be sure that the "External" keying source is selected in
     the Ports menu.
     
     


                                                                      Page 16

     9. Circuit Diagrams for External Connections
     --------------------------------------------
     
          a. Using an External Hand Key
          -----------------------------
     
     
          To RS-232 DSR    o------------+
            (Pin 6) or CTS              |
            (Pin 5)                     o
                                          /  Morse Telegraph Key
          (COMPUTER)                     /   ("Straight" Key)
                                        o
                                        |
          To RS-232        o------------+
          Pin 7 (*)
          GND
     
               * Due to variations among manufacturers, you may have to
               experiment to determine the correct pins
     
          b.  Connecting to a Receiver
          ----------------------------
     
               No one has submitted a circuit for connection to a
          radio receiver, but the following is the way it is done in
          concept.
     
     
                  +-----------+    +-----------+       +-----------+
          DSR/CTS |           |    |           |       |           |
          o-------+ Voltage   |    | Tone to   | Audio |           |
                  | Controlled+<---+ Voltage   +<------+   Radio   |
          o-------+ Switch    |    | Converter |       |           |
          GND     |           |    |           |       |           |
                  +-----------+    +-----------+       +-----------+
     
          The connections to the computer are the same as for the
          straight key above.  The voltage-controlled-switch can be a
          transistor or relay. The tone to voltage converter can be a
          phase locked loop, which is available in chip form.  The
          details are left to the user, but circuits that can be used
          or adapted can be found in the ARRL Handbook and other
          similar sources.
     
          c. Driving a Transmitter or Other Device
          ----------------------------------------
     
               The following circuit designed by John Swancara,
          WA6LOD, can be used to drive a keyer, code oscillator, or a
          transmitter. It is described in QST Magazine, February,
          1990, page 36.  A similar circuit was provided by John
          Dilks, K2TQN.
     


                                                                      Page 17

               If these connections do not work, first check the Port
          settings in the Options menu.  Then check your computer's
          RS-232 information in case you computer uses something
          different from the standard.
     
     
                                  +-----------------------+
                                  |  Radio Shack TIL-113  |
                                  |                       |
                                +-+-+                   +-+-+
                                ³   ³                   |   |
          RS-232 Signal   o-----+ 1 +---+    +----------+ 6 +-o NC
          ground (Pin 7)        ³   ³   |    |          ³   ³
                                +-+-+   |    |          +-+-+
                                  |     |    |            |
                                  |     +    |            |
                                  |    \ /   |            |
                                  |     v    |            |
                                  |     -    |            |
                                  |     |    |            |
                                  |     |    |            |
                           D1     |     | \  |            |
                                +-+-+   |  \ |          +-+-+
          RS-232    R1      /   ³   ³   | \  |          ³   ³
          Pin o--+--\/\/--|< +--+ 2 +---+  \ |      +---+ 5 +-o To
          4      |          \   ³   ³        |          ³   ³   Positive
                 |              +-+-+        |     /    +-+-+   Keying
                 |                |          |   |/       |     Line
                -+-  C1           |          |   |        |
                -+-               |          |   |        |
                 |                |          +---+        |
                 |                |              |        |
                 |                |              |        |
                 |                |              |\       |
              o--+                |                \      |
                 |              +-+-+               _|  +-+-+
                 |              |   |                   |   |
                ---        NC o-+ 3 |               +---+ 4 +-+-o To
                 -              |   |                   |   | |   Trans-
                                +-+-+                   +-+-+ |   mitter
                                  |                       |   |   Chassis
             Board                |                       |   |
             Ground               +-----------------------+   |
                                                              |
                                                             --- Interface
                                                              -  Board
                                                                 Ground
     
                                 D1  = 1N914
                                 R1  = 1K Ohm, 1/4 Watt
                                 C1  = 0.01 Microfarad, 50 Volt
                                 DTR = Data Terminal Ready pin
                                 NC  = no connection
     


                                                                      Page 18

          Note: (1) Voltage on pins 4 and 5 of TIL-113 should be kept
                    below 20 volts, and the current draw should not
                    exceed 100 ma.
     
                (2) The Philco ECG 3041 may be substituted for the Radio
                     Shack TIL-113.
     
          d. Using a Volume-Controlled Headphone
          --------------------------------------
     
               Splice a 50 ohm variable resistor and a headphone jack
          into the PC speaker line as shown below.  The headphone jack
          should break the speaker circuit and close the headphone
          circuit when the headphone plug is inserted.
     
                                   Headphone Jack
     
                 o--------+           o     o
                          |           |     |
                           \          |     |
            PC        50   / <--------+-------------+  /|
          Speaker     ohm  \                |       | / |   PC
            Line           /                |       |/  |   Speaker
                          |                 |       |\  |
                          |                 |       | \ |
                 o--------+-----------------+-------+  \|
     


                                                                      Page 19

          e. Using an External Oscillator
          -------------------------------
     
     
               Following is a simple code oscillator driven from the
          COM port of a PC designed by Jeff Furman, KD6MNP.
     
          DB-25
          FEMALE
                       1N4001
          +-----+
          |     |       |\ |
          |     +-------| \+-------+---+
          |  4  |       | /|       |   |
          |     |       |/         |   |  555
          |     |             +----+---+------+
          +-----+             |               |
          |     |             |    4   8      |
          |     |             |               |
          |  7  +------+------+ 1             |
          |     |      |      |               |
          |     |      |      |               |
          +-----+      |      |               |
                       |      |    6   2   3  |             1/8" stereo
                       |      +----+---+---+--+             headphone jack
                       |           |   |   |
                       |    ||     |   |   |    ||
                       +----++-----+-+-+   +----++------------+---- V    |
                       |    ||       |     |    ||            +-- v      |
                       |             |     |                             |
                       |              \/\/\                   +----------+
                       | 0.001 uF      680K   0.01 uF         |                               ³   film        680k   ceramic or      ³
                       | film          ohms   ceramic or film |
                       |                                      |
                       +--------------------------------------+
     
     
                       This easily fits inside the DB-25 shell.
                       Adjust the 680k ohm resistor to change the pitch--
                       higher value for lower pitch, etc.
                       Decrease the value of the 0.01 uF cap. for lower volume.
     
                       Super Morse Options|Ports settings:
     
                            Keying Port  : <your choice from what's available>
                            Output Keying: ON
                            RS-232 Output: RTS
                            Output Sense : -
     


                                                                      Page 20

          f. Using an External Sound Output
          ---------------------------------
     
               The following circuit was submitted by Bruce G.
          Kinney, San Jose, CA
     
                                       +------------------+
                          30K    Shield|                  |
               Pin 20 o--\/\/\/--+-- O + MOD IN           |      /|
                                 |   | |               O  +---- / |
                         .68uf  -+-  | |               U  |   <   | Speaker
                                -+-  | |               T  +---- \ |
                                 |   | |                  |      \|
               Pin 7  o----------+---+-+ GND              |
                                       |                  |
                                       +------------------+
                                          LEADER 1300S
                                        Function Generator